## Slide 1: Unit 2 Cellular Architecture
Dr.M.Manimegalai

## Slide 22: Cellular concept

## Slide 64
Interference and system capacity

## Slide 80: Coverage & Capacity Improvement
As the demand for wireless service increases, the no. of channels assigned to a cell is not sufficient to support the users.
To provide more channels per unit coverage area
Techniques used to improve coverage and capacity
  Cell Splitting
  Cell Sectoring
  Coverage Zone

## Slide 81: 1.CELL SPLITTING
Cell Splitting :It is the process of subdividing the congested cell
into smaller cells.
Each of the smaller cells will have their own base station with a
reduction in antenna height and transmitted power.
The smaller cells are known as Microcells.
Cell Splitting increases the capacity of the cellular system as it increases the number of times the channels are reused
The increased number of cells would increase the number of clusters over the coverage region, which in turn increase the number of channels, and thus capacity in the coverage area
Cell Splitting allows the system to grow by replacing large cells with smaller cells without changing the co-channel re-use ratio Q

## Slide 91: Cell Splitting Drawbacks
In practice not all cells are split simultaneously, therefore we may have cells of different sizes.
Also the handoff between the cells and microcells has to be taken care off so that high speed and low speed mobiles are equally served.
Decreasing cell size results in more handoffs per call and higher processing load per subscriber. Thus, the handoff rate will increase exponentially

## Slide 92: 2.Sectoring
The co-channel interference in a cellular system can be decreased by replacing the omni directional antenna at the base station by several directional antennas, each radiating within a specified sector.
The process of reducing the co-channel interference and thus increasing the capacity of the system by using directional antennas is known as Sectoring.
In general a cell is partitioned into three 120 degree sectors or six 60 degree sectors.
When sectoring is employed, the channels used in a particular cell are broken down into sectored groups and are used only in a particular sector.

## Slide 93: Sectoring improves S/I

## Slide 97: 1200 Sectoring

## Slide 98: 600 Sectoring

## Slide 99
The Improvement in (S/I) suggests that the minimum required (S/I) of 18 dB can be easily achieved with 7-cell reuse by employing 120 degree sector technique when compared to 12-cell reuse
Therefore Sectoring reduces interference and increases the capacity by an amount of (12/7)
i.e 1.714
In general, the reduction in interference by sectoring enables planners to reduce the cluster size N, and provides an additional freedom in assigning channels

## Slide 100: Disadvantages:
Increased number of antennas at each base station
Decrease in trunking efficiency due to channel sectoring at each base station
As sectoring reduces the coverage area of a particular group of channels, the number of handoffs increase.

## Slide 103: ADVANTAGES OVER SECTORING
As the mobile travels from one zone to another within the cell, it retains the same channel.Thus, a handoff is not required at the MSC
A given channel is active only in the particular zone in which the mobile is traveling and hence the base station radiation is localised and interference is reduced
The co-channel interference is also reduced as a large base station is replaced by several lower powered transmitters on the edges of the cell

## Slide 104: Techniques used to expand the capacity of Cellular system
Increasing the amount of spectrum used
More efficient modulation formats & coding
Better source coding
Discontinuous voice transmission
Multiuser detection
Adaptive modulation and coding
Reduction of cell radius
Use of sector cells
Use of an overlay structure
Multiple antennas
Fractional loading
Partial frequency reuse